## Slide 1
Proposed MOCOPA Change
30 March 2021

## Slide 2: Installing isolators
The DCUSA Safe Isolations Working Group have frequently discussed the issue around the removal of the mains fuse by unauthorised parties.
At present only MOCOPA parties can be authorised to undertake this work.
Operators must either be authorised via NSAP or by the DNO
We are aware of non-authorised parties removing the mains fuse, one of the reasons cited is the industry complexity and co-ordination particularly where bulk refurbishment is required.
Safe Isolations WG has discussed several options but to date have not agreed a way forward.
The AMO are proposing a change to MOCOPA

## Slide 3: Background
It has become apparent over the last few years that the fitting of an isolator between the electricity meter and the consumer unit has been frustrated by the current rules which require the work to be undertaken on the instructions of the electricity supplier appointed to that property or where the Operator is already appointed to that property. This has caused many issues where, for example, a local authority wishes to refurbish many dwellings but first needs the consent of the electricity supplier. There are currently over 100 licensed domestic electricity suppliers.
There have been numerous complaints into the industry including via trade bodies such as Electrical Safety First. It is believed that there are many hundreds of occasions where a non-MOCoPA party breaks specified seals on DNO and Supplier owned equipment to complete their work. Whilst this is a breach of ESQCR there has been no enforcement as the industry has not been able to provide a simple solution that can be adopted by all stakeholders.
The installation of Electric Vehicle chargers and other customer generation equipment has seen the number of unauthorised breaking of specified seals increase, with the uptake of EVs increasing year-on-year then it can be reasonably assumed that the associated unauthorised breaking of seals will also increase.
Within the industry there is a programme to enable Multiple Dwelling Units (MDUs) to engage with the smart metering installation programme. This will involve installing additional equipment in various MDU locations, it is feasible that in some of these locations it would be advantageous to install an isolator switch.
It should be noted that only MOCoPA parties have the authority to break Distribution seals and remove the main fuse. This proposed change maintains that requirement.

## Slide 4: Proposed Change
MOCOPA Operator Scope (Page: 51 version 4.9)
A MOCOPA Operator is only able to break the seals on and work upon Metering Equipment and Distribution Business Equipment, if: at the relevant Metering Point, they are the appointed MOCOPA Operator and are instructed by the electricity Supplier appointed to the relevant Metering Point; or, for whole current metering only, at the relevant Metering Point, they are not the appointed MOCOPA Operator, but they are required, by ​the property owner, or with the express permission of the property owner , a third Party electricity Supplier or by the gas Supplier responsible under the Use of System Agreement for the equipment used for the communications with gas meters at the Site, to carry out the following work at the Metering Point (excluding replacing meters):
i. Minimal reposition of third Party Supplier’s meter in communal meter position, to accommodate space for appointed smart meter installation;
ii. Work on looped neutral(s) on Metering Equipment;
iii. Work on a shared supply;
iv. Investigation/remedial revenue protection work;
v. Installation of an isolator; and/or
vi. Install, operate, inspect, maintain, repair, renew, reposition, replace and/or remove equipment used for communications with gas meters at the Site (including minimal repositioning of electricity metering equipment as allowed under Use of System Agreement

## Slide 5: Solution Comment
This issue has been recognised at the DCUSA Safe Isolations Working Group and previously agreed as an issue at the BEIS Smart Metering Operations Group (SMOG) The removal of specified seals and fuses by non-authorised parties is both a health & safety issue and a contravention of ESQCR. The proposed solution maintains the requirement for party who has acceded to MOCoPA to undertake the activity but broadens who can instruct that party to undertake the work
As an example, a local authority or housing associate could contract with a MOCOPA party of their choice based on a commercial agreement. This could be either a Distributor party or an Operator party.
We believe that this maintains the integrity of ensuring that only MOCOPA parties can undertake this work.
This could potentially lead to an increase in MOCOPA Operator parties but it should be noted that as from September 2021 this would be an accession to REC
This solution does not preclude the Safe Isolations WG from developing a solution such as electrician registration.