## Slide 1: Site-Specific Shared Network Asset Categories
Clarification sought on current practice

## Slide 2: Background
As per DCUSA, under the EDCM: A Connectee's notional site-specific shared network asset value is the value of network assets that are deemed to be used by that Connectee, other than sole use assets.
DCUSA defines five network levels as below:
  Level 1 comprises 132 kV circuits.
  Level 2 comprises substations with a primary voltage of 132 kV and a secondary voltage of 22 kV or more.
  Level 3 comprises circuits of 22 kV or more but less than 132 kV.
  Level 4 comprises substations with a primary voltage of 22 kV or more but less than 132 kV and a secondary voltage of less than 22 kV.
  Level 5 comprises substations with a primary voltage of 132 kV and a secondary voltage of less than 22 kV.
The category code defines which levels are used beyond the SUA, which assets are paid for, and through which tariff element.

## Slide 3: The issue
This query concerns an issue of categorisation of an EDCM connection where there is some ambiguity in the legal text.
In the case of a customer connected to a bulk supply point substation but with a connection that is banked with another circuit such that both share the same 33kV circuit breaker, what is the correct EDCM category under schedule 17/18?
The hypothetical connection is illustrated to the right:
In this situation are the customers 1100, or 1110?
We would like to understand what the generally accepted view is on this.
Customer 1
Customer 2
132kV
33kV

## Slide 4: Legal text definitions
Customers are categorised into various categories including the below:
The ambiguity in this case arises because the customer is connected ‘at the substation’ but not directly to the busbar (the ‘secondary side of the substation’), instead there is a piece of shared 33kV circuit (the shared circuit breaker).
Depending on interpretation, either category might fit this case.
Category 1100 | Point of Common Coupling at 22 kV or more on the secondary side of a substation where the primary side is attached to a 132 kV circuit.
Category 1110 | Point of Common Coupling at a voltage of 22 kV or more, but less than 132 kV, not at a substation, fed from a substation whose primary side is attached to a 132 kV distribution circuit.

## Slide 5: DCUSA Illustrations
DCUSA provides this illustrations of the various categories.
The query concerns 1100 and 1110.

## Slide 6: Illustration detail
Zoomed in the relevant categories are illustrated to the left.
Blue is 132kV, green 33kV.
1100
1110