## Slide 1: Working Group Slides for DCP443 (Request H03-5)
July 2025

## Slide 2: Summary
A customer who exceeds their capacity will not necessarily impose costs on higher voltage assets.
Reducing unit rates make time-of-use signals weaker.
Risk of revenue under-recovery if behavioural response is achieved.
CDCM considers ultra-long run cost of peak demand. How exactly does capacity exceedance increase network costs?

## Slide 3: Objectives
There were two objectives outlined in the attachments sent:
“To amend excess capacity charges so that they are set in order to drive the correct customer behaviours” – Attachment 1 CP form
  Capacity charges and excess capacity charges are currently the same in the CDCM. This means that customers are not incentivised to upgrade their capacity or avoid exceeding their capacity.
  Exactly how “correct customer behaviours” is defined could be subjective.
“Ensure costs related to demand due to excess capacity are reflected in the Excess Capacity charge” – DCP 443 Modelling Specification
  Currently costs are reflected in both excess capacity (for local assets) and unit rates (for higher voltage assets).
  Whether costs are “related to demand due to excess capacity” is difficult to define.
It is also important to note that these objectives may conflict with each other - a specific methodological change may achieve one but exacerbate the other.

## Slide 4: Proposed change: step 1
“Enhanced standing charge factors are introduced which calculate a new higher differential excess capacity charge. The charge is higher than the normal capacity charge because the standing charge factors extend to higher voltage level assets. “
  Arguably this helps to achieve the first objective because it increases the excess capacity charge relative to the capacity charge. This drives “correct” (first objective) customer behaviours since customers are penalised for exceeding their capacity. Customers who regularly exceed their capacity will therefore be incentivised to upgrade their capacity or change their behaviour.
  However, a customer who exceeds their capacity will not necessarily impose costs on higher voltage assets. For example, a customer who exceeds their capacity could cause constraints locally on the network. However, if the timing of this exceedance does not coincide with peak demand higher up the network (due to diversity), then this may not actually increase costs.
  As a result, this is not necessarily cost-reflective. The same penalty is applied to customers no matter when they exceed their capacity (and thus regardless of the impact on the higher voltage network). So, while this may achieve the first objective with respect to the local network voltage levels, it may not create any benefit for the higher voltage levels of the network.
  It also doesn’t necessarily achieve the second objective for the same reason. A customer that exceeds their capacity will be charged extra in line with the proposed change. However, if this increase in demand does not coincide with increased peak demand on the higher voltage networks, then it is not associated with an additional cost at that part of the network.

## Slide 5: Proposed change: step 2
“Unit rates are adjusted downwards to reduce price signals by an amount equal to the extra revenue expected to be collected due to the new differential element of the excess capacity charge. This ensures there is no overall impact on the level of costs reflected by forward looking charges in total. “
  Can this be justified as cost-reflective, based on how excess capacity affects higher voltage levels (previous slide)?
  Furthermore, would this encourage “incorrect” customer behaviour by making time-of-use signals weaker? Adjusting unit rates downwards means that price signals are less time-dependent.
  There is also a risk associated with this aspect of the proposed change. If an increase in excess capacity charge does encourage a behavioural response from customers and they avoid exceeding capacity, then the decrease in unit rates will mean that DNOs will under-recover revenue.

## Slide 6: CDCM long-term cost-reflectivity
The CDCM considers the ultra-long run (or average) cost associated with peak demand, so there is arguably no meaningful distinction between capacity and exceeded capacity. Since, in the ultra-long run, the DNO is assumed to increase the size of the network to accommodate the excess.
The working group should consider how exactly customer exceedance of capacity agreements increases network costs, and how this can be reflected within the CDCM’s approach. For example, exceedance of capacity might cause reinforcement requirements to be accelerated or even lead to security or safety issues. The CDCM does not currently provide a means for estimating the cost impacts of these outcomes.

## Slide 7: Questions asked by the Working Group
“Is there a more cost reflective way of reducing the unit rates to reflect the cost move to excess capacity charges? i.e. Could there be an approach which truly reflects the costs moved to excess capacity that is more granular than the use of three single scaling factors for each of LV, LVS and HV?”
The proposed increase in excess capacity charge is not based on an assessment of cost associated with capacity exceedance. So, can it be argued to be cost-reflective?
The reduction in unit rates is purely done to balance the revenue recovered from this increase in the excess capacity charge. So, it is arguable that any reduction in the unit rates for this reason isn’t cost-reflective.
This suggests that another solution may be necessary. The solution should try to consider the actual cost to the network of exceeded capacity.

## Slide 8: Disclaimer
This document is issued for the sole use of the Customer as detailed on the front page of this document to whom the document is addressed and who entered into a written agreement with TNEI. All other use of this document is strictly prohibited, and no other person or entity is permitted to use this report unless it has otherwise been agreed in writing by TNEI. This document must be read in its entirety and statements made within may be based on assumptions or the best information available at the time of producing the document and these may be subject to material change with either actual amounts differing substantially from those used in this document or other assumptions changing significantly. TNEI hereby expressly disclaims any and all liability for the consequences of any such changes. TNEI also accept no liability or responsibility for the consequences of this document being relied upon or being used for anything other than the specific purpose for which it is intended, or containing any error or omission which is due to an error or omission in data used in the document that has been provided by a third party. This document is protected by copyright and may only be reproduced and circulated in accordance with the Document Classification and associated conditions stipulated or referred to in this document and/or in TNEI’s written agreement with the Customer. No part of this document may be disclosed in any public offering memorandum, prospectus or stock exchange listing, circular or announcement without the express and prior written consent of TNEI. A Document Classification permitting the Customer to redistribute this document shall not thereby imply that TNEI has any liability to any recipient other than the Customer. Any information provided by third parties that is included in this report has not been independently verified by TNEI and as such TNEI accept no responsibility for its accuracy and completeness. The Customer should take appropriate steps to verify this information before placing any reliance on it.