## Slide 1: Associated Distribution Systems
Impact on Use of System Charging?
Mike Smith
  Metering Analyst, Elexon

## Slide 2: BSC measurement requirements
Section K of the BSC require certain flows to be measured and recorded for Settlement purposes
Section K defines:
  an Import (I) and an Export (E) and these need to be measured at Boundary Points (BPs) to the Total System
import (i) and export (e) and these need to be measured at Systems Connection Points (SCPs)
  Total System? - Transmission System (TS), plus each Distribution System (DS) plus Offshore Transmission System User Assets (OTSUA)
  BP? - a connection between the Plant & Apparatus (P&A) ‘of’ a BSC Party (e.g. Supplier (of a Customer or Third-Party Generating Plant), or Generating Plant owned and operated by a BSC Party, that is not considered part of the Total System, and the P&A of a BSC Party (e.g. LDSO/IDNO/NETSO) that is considered part of the Total System
  SCP? – a connection between two Systems (i.e. between the TS and a DS, at a Grid Supply Point (GSP) and DS to DS, where the DSs are in different GSP Groups, at Distribution System Connection Points (DSCPs))

## Slide 3: BSC metering requirements
Section L
  Metering Equipment - installed, commissioned, operated and maintained to measure and record Active Energy and, where relevant, Reactive Energy, flowing at BPs (and SCPs)
  Codes of Practice (CoPs) - overall accuracy to be maintained, within certain limits, at a certain points called Defined Metering Points (DMPs)
  DMPs now, since CP1479 ‘Updates to the Defined Metering Points in Codes of Practice 1, 2, 3, 5 and 10’, all coincide with BPs or SCPs
  If overall accuracy cannot be maintained at the DMP, or loss compensation is required to do so, or there are any other Metering Equipment non-compliances, a Metering Dispensation is required to be approved by the BSC Panel or Elexon (limited to shared circuits with only loss compensation required)
  Active Energy requirements - defined in the CoPs for Settlement purposes (and Use of System (UoS) charging)
  Reactive Energy requirements - defined for UoS charging only (the BSC does not use this data for Settlement)
  Data Collectors collect, validate and estimate (where applicable) metered data and pass this to the System Operators (NETSO and LDSOs/IDNOs), as well as Registrants of BP Metering Systems.
  NETSO and LDSOs/IDNOs use this metered data for UoS charging/system planning, etc.
  Registrants of BP Metering Systems use this metered data for Settlement and, where the Settlement Meter doubles as a billing meter, to bill (Customers) or pay (Generators) for Active Energy use or generation and bill for UoS charges (when passed through them)

## Slide 4: Modification Proposal P062
P062 ‘Changes to Facilitate Competitive Supply On The Networks Of New Licensed Distributors’ introduced the concept of Associated Distribution Systems (ADS)
Definition:
“means, in relation to a Licensed Distribution System Operator (or SMRA, as the case may be), a Distribution System:
(i) which is not operated by a Licensed Distribution System Operator; and
(ii) in respect of which all the entry/exit points are subject to registration in such Licensed Distribution System Operator's (or SMRA's) SMRS;
and, for these purposes, 'entry/exit point' means a point at which electricity may flow on to or off such Distribution System other than from or to the Transmission System or another Distribution System”
This means ADS’s are considered to be part of the Total System so flows from the LDSO’s DS to the ADS are not required for Settlement purposes (but may still be required for UoS charging - private arrangement to collect this metered data)
The Customer’s/Generators metered data will be used for Settlement purposes and, presumably should be used for UoS charging purposes?

## Slide 5: UoS impact?
Customers/Generators on certain ADSs may be being charged UoS based on the voltage level at the point at which the ADS connects to the LDSO/IDNO network, e.g. 33kV, using the Extra High Voltage (EHV) Charging Methodology (EDCM)
The Customers/Generators may be connected at a different voltage on the ADS and expect to be charged UoS based on that voltage level, e.g. 11kV using the Common Distribution System Charging Methodology (CDCM)
Elexon’s view is that these Customers/Generators should be treated the same as any other Customers or Generators that are connected directly to the LDSO/IDNO’s network, and not via an ADS, because an ADS is a DS and part of the Total System, i.e. based on the voltage level where they connect to the ADS
Do you agree?
If so, what changes need to be made to industry Codes (DCUSA, BSC, etc.) or the Ofgem approved Charging Methodologies to facilitate this?

## Slide 6: Thank you